| HELPFUL ADVICE No.2 |
| --- |
| How your central heating programmer or time clock works |
| A programmer allows you to switch the hot water and heating system in your home on or off. It also allows you to set the periods during the day or night when you wish hot water to be available or your home to be warm; therefore ensuring both suits your lifestyle. A time clock looks almost identical to a programmer, but controls only your heating. They are fitted in flats and bungalows fitted with combination boilers, where it is not possible to have the heating on separately from the hot water. |
| DISPLAY A digital clock showing the time or programme setting. |  |
| ON/OFF MARKER Guide to the information on display. |  |
| HEATING INDICATOR Lit up when the heating is on. |  |
| OVERRIDE BUTTON Switches the heating on or off without altering the program settings. | EXTRA HOUR BUTTON Switches the heating on for up to 3 extra hours as a ‘one-off’ for extra flexibility. | SETTING SLIDER 2 sliders on a programmer, allowing you to choose how you wish your hot water and heating to operate. Only 1 on a time clock, for the heating. | RESET BUTTON Resets the programmer to its original built-in setting. | PROGRAMME CONTROLS Used to set the clock and programme times. |
| In the event of an electricity supply failure, the unit has a built-in battery to ensure everything still works to your settings until the power is restored. |