HELPFUL ADVICE No.4

Indications of a faulty hot water thermostat

This leaflet is to provide advice and guidance if you have a hot water cylinder in your home. If you have a combination or ‘combi’ boiler installed you will not have a hot water cylinder and this will not apply to you. The Health and Safety Executive (HSE) has issued a safety alert to raise awareness of a rare, but potentially serious risk from domestic hot water systems which include a fixed all-electric or part electric immersion heater in conjunction with a plastic cold water storage cistern or ‘tank’ located in the roof space. The alert follows two similar fatal accidents in the four years up to 2007 where a large volume of near boiling water poured through a bedroom ceiling on to the occupants sleeping below. The cause was a combination of faults on the system and an overheating immersion heater that triggered a volume of hot water to enter the plastic storage cisterns in the roof space above. There are a number of warning signs that could indicate a possible thermostat failure and overheating of the hot water in the cylinder. They include: Excessively hot water coming out of the hot water taps A very hot cylinder or airing cupboard Hot water coming out of cold water taps Excessive noise or ‘bubbling’ from the hot water cylinder Moisture or steam in the roof space/airing cupboard Remember, these warning signs can occur on any heating system with a hot water cylinder, regardless of whether it is gas, oil, solid fuel or electric. If you notice any of the above warning signs, you should: Turn off the immersion heater switch and/or the central heating boiler switch Run off all of the stored hot water, being mindful that the temperature of the water may be extremely hot Contact the Repairs Desk by telephone on 01530 454635 or by email on repairs@nwleicestershire.gov.uk This leaflet is one of a series in our ‘Helpful Advice’ sheets to help you understand how to use common appliances and services within your home. Others in the series include: N0.1 How your consumer unit works N0.2 How you central heating programmer or time clock works N0.3 How your gas boiler works All are available from the Repairs Desk